# DSP Code Standards (DRAFT)

## General Comments

Much of the DSP code structure is determined by the architectures of our several modules.  A substantial portion of the architecture is shared among multiple modules.  Thus it will enhance reliability and ease of development to establish a set of coding conventions that allow us to share source code between architectures whenever and wherever possible.  The follow standards are an attempt to enable such a code structure.

The architecture of each module is built around a standard set of boards.  These are:

- Analog (or, front-end) boards

- Timing board

- Digital board

We propose to

## File Naming Conventions

### Header Files

Header files specific to boards will have special naming conventions as follows:

- Analog Boards

  - ana_6048_xxx.h where 6048_xxx indicates the design drawing number

  - BPM analog board (1st gen. module): 	ana_6048_100.h

  - BPM analog board (2nd gen. module): 	ana_6048_114.h

  - FLM analog board (v1):            	ana_6048_116.h

  - BSM analog board:                          	ana_6048_116.h

- Timing Boards

  - tim_6048_xxx.h where 6048_xxx indicates the design drawing number

  - Timing board (1st gen. module):	tim_6048_101.h

  - Timing board (2nd gen. module):	tim_6048_115.h

- Digital Boards

  - dig_6048_xxx.h where 6048_xxx indicates the design drawing number

  - SHARC digital board:	dig_6048_102.h

  - TS101 digital board:	dig_6048_113.h

### Code Files

DSP source code for the various architectures will fall in 3 categories:

- Code that is specific to a particular DSP

- Algorithm code that can be shared across DSPs

- Algorithm code that can be shared between the control system and one or more of the DSP architectures

Naming conventions for these different categories will be as follows:

- Code that is specific to the SHARC DSP architecture will carry the prefix sh_

- Code that is specific to the TS101 DSP architecture will carry the prefix ts_

- Code that can be shared across DSP architectures will carry the prefix dsp_

- Code that can be shared between the DSPs and control system programs will carry the prefix of the control system library to which they belong and will live in a sub-directory called “shared” within that library.  This naming convention will take precedence over the three preceding rules.

## Hardware-Level Macro and Variable Naming Conventions

Macro definitions referring to specific board types will follow the convention:

- Analog board macros will start with the prefix ANA_

- Timing board macros will start with the prefix TIM_

- Digital board macros will start with the prefix DIG_

Global variable names associated with specific board types will follow the convention:

- Analog board variables will start with the prefix ana_

- Timing board variables will start with the prefix tim_

- Digital board variables will start with the prefix dig_

- EXCEPT when the variables are pointers.  In this case, a p_ will precede the ana_, tim_, or dig_ prefix to indicate a pointer type.  In fact, most variables associated with specific board types will be pointers (to registers or memory) so the most common situation will be

## Examples