## Slide 1: FRACTIONAL ARC TEST GIRDER DESIGN REVIEW

## Slide 2
FRACTIONAL ARC TEST GIRDER
PROTOTYPE GIRDER
Same design except 6’’ longer to accommodate half magnet BDH

## Slide 3
+2’’
-2’’
± ∞’’
(T-bolt slides in slot)
± .5’’

## Slide 4
±.25’’
±.13’’
±.5’’
Each magnet is supported on three points with three tie-down bolts

## Slide 5
Chamber location/mounting
These angles (blue) locate BPMs with shoulder screws
These angles (yellow) just provide support. Have oversized holes to allow for small misalignment of BPMs
Chamber is fixed in location on plate.

## Slide 6
Water Tubing
Water hoses and beam instrumentation cable feed through here
Brass water manifold

## Slide 7
Survey/Shipment
Cornell ships vacuum chamber to BNL.
BNL assembles magnets and chamber to plate.
BNL ships assembly at left to Cornell (un-surveyed).
Cornell receives Rexroth stand assembly from outside vendor.
Cornell joins plate to Rexroth stand.
Cornell does survey and positioning of magnets relative to chamber.
Cornell surveys/positions stand and plate into ring.
Workflow

## Slide 10
Deflection Analysis
-QF, BD = 100 lb. Ea (actual weight 91 lb.)
-BDH = 15 lb.
-Supported by Rexroth

## Slide 12
Locate mount for FARO survey arm.
Used to survey magnets in place.