## Slide 1: CBETA bunch pattern and BPM trigger generator

## Slide 2
Clock input
(41.9 MHz)
n
R[7..0]
Pattern Repeat Clock
(41.9 MHz / R)
Divide by n
R typically =
44 or 88
n
Divide by n
N[23..0]
Injection Start Clock
(as low as 1 Hz)
z
Delay by z
Z[3..0]
CLK
START
CLK
M[18..0]
Number of bits in trigger pattern
R[7..0]
Injection Start Clock Delayed
by Z 41.9 MHz periods
To LASER
OEM
LASER Trigger Pattern Generator
START
CLK
Number of bits in repeat pattern
BPM Trigger
BPM Trigger
Pattern Generator
Number of total triggers
Trigger pattern
P1[127..0]
Trigger pattern
P2[127..0]
Reset
Done
Reset
Mode
Mode
BPM Trigger Mode
0: One trigger on START
1: Trigger pattern until Reset
Trigger Pattern
The trigger pattern will be implemented as a shift register for the output trigger.
When a START pulse is received, the trigger pattern register Px is shifted to the output (bit 0 first) until R triggers have occurred. Then the trigger pattern repeats.
After a total number of M triggers are generated the Done output is asserted which halts and resets both pattern generators.
IN
OUT
Enable Time (seconds)
LASER Trigger Enable Timer
T[16..0]
Enable START
Software
push-button
Laser Trigger Enable Timer
This timer is used to prevent the laser from being enabled accidentally for an extended period of time. The operator initiates the laser triggers via a software pushbutton. After the timeout period (in seconds) the laser triggers will be inhibited. Maximum timer limits must be controlled.