## Weekly Tuesday Inspection Checklist-CHESS IDLE

Operator on Shift:

- All Secondary Gate Valves should be closed during Open Access

- BEFORE Open Access Ends, verify tunnel lights are off at C, D, F lines and G cave and all doors on Terranova racks in tunnel are closed

Signals for the past week: (complete by 10am)

- All 7 Day Buttons

- Note Any Missing Signals

- Print out plots of suspicious signals for distribution to the appropriate person

At Each Station and G-Cave:

- Printout motor positions at each station, ops, and G-cave (prout we) & add printouts to binder in Ops

In the Tunnel: (complete by 10am)

- Vacuum/clean around ends of undulator magnets, if they are installed (4 spots)

- Water leaks

- Ion pump controllers

- Loose wires

- Other obvious problems (look and listen)

- Look for missing bus covers, alert CESR operator and post webboard and ELOG notes.

- Turn off lights by C, D, and F lines and close all tunnel electronics racks as you go

At Operations

- On EPICS Monitors:

- Check for T.C. failures/overtemp

- Check for ion pump trips

- Check for disconnected signals/any other errors

- Remove group dosimeter log sheets weekly and individual dosimeter log sheets when they are full from binder, give to Dwight Widger

- Ensure broken equipment bench in ops is empty by either fixing equipment or giving to appropriate staff to fix

- Vacuum computer fans & electronics

Misc. Stuff

- Inventory Radiation Sources

- Glovebox: Check display screen for any alerts or alarms (box normally operates between 1-5mbar). Report anything suspicious (unlabeled vials, spilled materials, etc)

- Check ice machine in cold room – break up/empty out large chunks as necessary

- Check chem. room for obvious problems

- Run water through eye washes until it is clear.  4 locations: G line chem room, main chem room, CHESS Ops, room off of F1

- Check door intercoms (5th floor and loading dock)

- Clear clutter from Ops/Prep area.

Post all of your findings to the Webboard