## Weekly Tuesday Inspection Checklist-CHESS RUNNING

Operator on Shift:

- BEFORE Open Access begins, close all Secondary Gate Valves

- BEFORE Open Access ends, verify tunnel lights are off at C, D, F lines and G cave and all doors on Terranova racks in tunnel are closed

- DURING White Key Access, open all secondary gate valves

Signals for the past week: (complete during OWL shift)

- All 7 Day Buttons

- Note Any Missing Signals

- Print out plots of suspicious signals for distribution to the appropriate person

At Each Station and G-Cave:

- Look for badges, forms, parking permits, burn paper

- Move 2 “occupied” area badges from A1 user area to badge rack at Ops

- Print out motor positions at each station, ops, and G-cave(prout we) & add printouts to binder in Ops

- Check kapton window in A1, mylar window in F1 and replace if necessary

- Check kapton window at I0 in F1 and replace if necessary

- Check detector chiller fluid level in F2, and GE and Pilatus detectors if being used. Top off when necessary

In the Tunnel: (complete by 10am)

- Vacuum/clean around ends of undulator magnets (4 spots)

- Record D-line beamstop counter in vacuum labbook conference on webboard

- Water leaks

- Ion pump controllers

- Loose wires

- Other obvious problems (look and listen)

- Look for missing bus/magnet covers, alert CESR operator and post webboard and ELOG notes.

- Turn off lights by C, D, and F lines and close all tunnel electronics racks as you go

At Operations

- On EPICS Monitors:

- Check for T.C. failures/overtemp

- Check for ion pump trips

- Check for disconnected signals/any other errors

- Remove group dosimeter log sheets weekly and individual dosimeter log sheets when they are full from binder, give to Dwight Widger

- Ensure broken equipment bench in ops is empty by either fixing equipment or giving to appropriate staff to fix

- Vacuum computer fans & electronics

Misc. Stuff

- Inventory Radiation Sources

- Glovebox: Check display screen for any alerts or alarms (box normally operates between 1-5mbar). Report anything suspicious (unlabeled vials, spilled materials, etc)

- Check ice machine in cold room – break up/empty out large chunks as necessary

- Check chem. rooms for obvious problems

- Run water through eye washes until it is clear.  4 locations: G line chem room, main chem room, CHESS Ops, room off of F1

- Check door intercoms (5th floor and loading dock)

- Clear clutter from Ops/Prep area and experimental floor

F2 Cryo System

- Check drip pans and buckets on East roof; empty as necessary

Post all of your findings to the Webboard