ILC Damping Rings Component/Subsystem Specification

Part I – Classification Information

| Component Description: | Dipole magnet power cable |
| --- | --- |
| Component Location (beamline): | EDR, PDR I, PDR II | Lattice Version: | OCS6, 2006-06-30 |
| Document Number: | EDR-MAG-cbl-001 | Date: | 2006-08-03 |
| Prepared by: | Andy Wolski (Cockcroft) | email: | a.wolski@dl.ac.uk |
| Technical/Global System: | Magnets |  |  |
| Technical/Global System Contact: | John Tompkins (FNAL) | email: | jct@fnal.gov |
| DR Area System Contact: | Mike Zisman (LBNL) | email: | mszisman@lbl.gov |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Quantity per beamline | 22.6 km | [1] |
| Conductor | Copper |  |
| Electrical conductivity | 60(10-6 (-1m-1 |  |
| Density | 8920 kg/m3 |  |
| Conductor cost | Public version: no costs shown | [2] |
| Cable resistance | 0.0433 (/km |  |
| Cable diameter | 22 mm |  |
| Cable mass | 3.4 kg/m |  |
| Maximum current | 520 A | [3] |
| Voltage drop at maximum current | 22.5 V/km |  |
| Unit cost per metre | Public version: no costs shown |  |

ILC Damping Rings Component Specification

| Document Number: | EDR-MAG-cbl-001 | Date: | 2006-08-03 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings

Figure 1: Schematic Layout

ILC Damping Rings Component Specification

| Document Number: | EDR-MAG-cbl-001 | Date: | 2006-08-03 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

Table1: Dipole cables and cable lengths (see Figure 1).

| Cable | Region | Dipoles | Length |
| --- | --- | --- | --- |
| 1 | Arc 1 | 19 ( 6 m | 1636 m |
| 2 | Short Straight A & Arc 2 | 19 ( 6 m | 2134 m |
| 3 | Arc 3 | 19 ( 6 m | 1636 m |
| 4 | Arc 4 | 19 ( 6 m | 1636 m |
| 5 | Short Straight C & Arc 5 | 19 ( 6 m | 2134 m |
| 6 | Arc 6 | 19 ( 6 m | 1636 m |
| 7 | Arcs 1,2,3 & Short Straights A,B | 6 ( 3 m | 5904 m |
| 8 | Arcs 4,5,6 & Short Straights C,D | 6 ( 3 m | 5904 m |

Part IV – References

[1]	See Table 1.

[2]	London Metal Exchange: http://www.lme.co.uk

[3]	EDR-MAG-dip-001