ILC Damping Rings Component Specification Sheet

Part I – General Information

| Component Description: | Electron Damping Ring Quadrupole Magnets (Injection/Extraction Region) |
| --- | --- |
| Component Location (beamline): | EDR, PDR1, PDR2 |
| Document Number: | EDR-MAG-quad-003 (rev. 3) | Date: | 2006-08-17 |
| Prepared by: | Mark Palmer (Cornell) | email: | map36@cornell.edu |
| Technical/Global System: | Magnets |  |  |
| Technical/Global System Contact: | John Tompkins (FNAL) | email: | jct@fnal.gov |
| DR Area System Contact: | Jie Gao (IHEP) | email: | gaoj@ihep.ac.cn |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Quantity per beamline | 26 | [1] |
| Magnet Type Designation | Q60L300V3 (C-style?) |  |
| Names in MAD deck | QFINJ1, QDINJ1; 2*QFINJ2H, QDINJ2; QFINJ3, 2*QFINJ4H |  |
| Element Type | Quadrupole | [1] |
| Integrated strength k1L (¦max¦) | 0.310 m-1 | [1,2] |
| Effective length | 0.3 m | [1] |
| Slot length | 0.5 m | [3] |
| Pole-tip radius | 0.030 m | [1] |
| Max. Pole-tip field | 0.517 T | [1] |
| Alignment tolerance: x y s | Not yet specified 30 m Not yet specified |  |
| Angular tolerance: Pitch Yaw Roll | 0.3 mrad 0.3 mrad 0.3 mrad |  |
| Magnet Technology | Normal conducting |  |
| Operating Characteristics Field type Polarity type Control mode | Constant field Unipolar Individual |  |
| Coil resistance |  |  |
| Current at max strength |  |  |
| Power (max) |  |  |
| Unit Cost |  |  |

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-MAG-quad-003 (rev. 3) | Date: | 2006-08-17 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings

Field quality specifications for 0.050 m reference radius [4].  It should be noted that these field quality specifications, which were those used to validate the OCS design, specify errors at the reference radius for the PEP-II quadrupoles.  The specifications need to be re-evaluated at a suitable reference radius for an ILC quadrupole design.

| N | systematic field error | Random field error |
| --- | --- | --- |
|  | bn | an | bn | an |
| 3 | -1.24(10-5 | -1.15(10-5 | 7.61(10-5 | 7.25(10-5 |
| 4 | 2.30(10-6 | 1.41(10-5 | 1.32(10-4 | 1.27(10-4 |
| 5 | -4.30(10-6 | 6.20(10-7 | 1.50(10-5 | 1.62(10-5 |
| 6 | 3.40(10-4 | -4.93(10-5 | 1.65(10-4 | 3.63(10-4 |
| 7 | 3.00(10-7 | -1.02(10-6 | 6.70(10-6 | 6.60(10-6 |
| 8 | 6.00(10-7 | 3.80(10-7 | 8.90(10-6 | 6.60(10-6 |
| 9 | 6.00(10-7 | -2.80(10-7 | 4.60(10-6 | 4.90(10-6 |
| 10 | -6.17(10-5 | -5.77(10-5 | 2.46(10-4 | 2.33(10-4 |
| 11 | -2.00(10-7 | -1.80(10-7 | 4.20(10-6 | 3.50(10-6 |
| 12 | 3.60(10-6 | -6.53(10-6 | 3.48(10-5 | 3.66(10-5 |
| 13 | 6.00(10-7 | 1.20(10-6 | 9.20(10-6 | 8.60(10-6 |
| 14 | 1.00(10-6 | -7.40(10-7 | 4.76(10-5 | 4.46(10-5 |

Special notes about the damping ring quadrupoles:

- There are no changes to the magnet specifications for 500 GeV versus 1 TeV collider operation.

Part IV – References

[1]	MAD deck (OCS v6), 20 June 2006.

[2] The maximum field (absolute value) is specified for the strongest magnet in this family operating at 10% higher energy than the nominal damping ring design.

[3] Slot lengths have been defined by taking the shorter of:

1) Half of the distance to the nearest neighboring magnet

2) 0.25 m

and adding twice that value to the effective length of the magnet.

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-MAG-quad-003 (rev. 3) | Date: | 2006-08-17 |
| --- | --- | --- | --- |

[4]	The multipole component is defined by:

A. Wolski, J. Gao, S. Guiducci, “Configuration Studies for the ILC Damping Rings,” LBNL-59449, pp. 21-22 (February 2006).