# ILC Damping Rings Component Specification Sheet

# Part I – Classification Information

| Component Description: | Generic Damping Ring Quadrupole |
| --- | --- |
| Component Location (beamline): | EDR/PDR I/PDR II | Lattice Version: | OCS6, 2006-06-20 |
| Document Number: | EDR-MAG-quad-005 | Date: | 2006-07-12 |
| Prepared by: | Jin-Young Jung | email: | JYJung@lbl.gov |
| Technical/Global System: | Magnets |  |  |
| Technical/Global System Contact: | John Tompkins | email: | jct@fnal.gov |
| DR Area System Contact: | Mike Zisman | email: | mszisman@lbl.gov |

# Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Quantity per beamline | 747 |  |
| Length | 300 m |  |
| Pole-tip radius | 30 mm |  |
| Maximum pole-tip field in lattice | 0.470 T |  |
| Minimum pole-tip field in lattice | 0.107 T |  |
| Maximum design pole-tip field | 0.517 T | [1] |
| Total current per pole | 7000 Ampere-turns |  |
| Current density | 305.5 Amperes/cm2 |  |
| Number of turns | (0.25 5” coil) 4(10 |  |
| Current | 175 Amperes |  |
| Voltage | 3.83 Volts |  |
| Power per magnet | 2.68 kW |  |
| Cooling water power rise | 11(C |  |
| Cooling water flow rate | 0.228 gal/min |  |
| Field quality (dg/g) | 0.002% at r = 2.5 cm |  |
| Magnet efficiency | 97.2% |  |
| Core volume | 0.034 m3 |  |
| Core mass | 584.4 lb |  |
| Coil mass | 106.9 lb |  |
| Core cost | Public version: no cost information shown | [2] |
| Coil cost | Public version: no cost information shown | [2] |
| Assembly and test | Public version: no cost information shown | [2] |
| Unit Cost | Public version: no cost information shown |  |

# ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-MAG-quad-005 | Date: | 2006-07-12 |
| --- | --- | --- | --- |

# Part III – Other Parameters, Information, and Drawings

Field in poles ~ 1 T Field in yoke ~ 1.4 T

# ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-MAG-quad-005 | Date: | 2006-07-12 |
| --- | --- | --- | --- |

Part IV – References

[1]	Actual maximum design pole-tip field is 0.5688 T; the quoted value is the effective maximum design pole-tip field, allowing 10% reduction from end effects.

[2]	Scaled from ALS costs, plus inflation increase of 4% per year from 1989 to 2006.