ILC Damping Rings Component Specification Sheet

Part I – Classification Information

| Component Description: | Electron damping ring RF cavity cryomodule |
| --- | --- |
| Component Location (beamline): | EDR | Lattice Version: | OCS2, March 2006 |
| Document Number: | EDR-RF-cav-001 | Date: | 2006-10-09 |
| Prepared by: | Roberto Boni | email: | roberto.boni@lnf.infn.it |
| Technical/Global System: | Cavity Package/Cryomodule |  |  |
| Technical/Global System Contact: | Kenji Saito Norihito Ohuchi | email: | kenji.saito@kek.jp, norihito.ohuchi@kek.jp |
| DR Area System Contact: | Susanna Guiducci | email: | susanna.guiducci@lnf.infn.it |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| RF stations operational | 8 | (7) | [1] |
| Quantity cryomodules per beamline | 32 | (28) | [1] |
| RF Frequency | 650 MHz |  |
| Active length | 0.23 m |  |
| R/Q | 89 ( |  |
| Operating temperature | 4.5 K |  |
| Standby losses at 4.5 K | 30 W |  |
| Accelerating gradient | 6.33 MV/m | (7.2 MV/m) | [1] |
| Accelerating voltage | 1.45 MV | (1.66 MV) | [1] |
| Q at operating gradient | 1.0(109 | (0.9(109) | [1] |
| Cryo-RF losses per cavity | 23.6 W | (34.4 W) | [1] |
| Beam power per cavity | 109 kW | (125 kW) | [1] |
| Qext | 215(103 | (248(103) | [1,2] |
| Unit Cost per Cryomodule | Public version: no costs shown | [3] |

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-cav-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-cav-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

CESR Superconducting RF cryomodules [4]: Length = 112.8 in = 2.87 m Height = 84 in = 2.13 m Width = 57 in = 1.45 m Note: these dimensions are for 500 MHz cavities. Scaling for 650 MHz may (in the most optimistic case) reduce the dimensions by approximately 20%.

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-cav-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part IV – References

[1]	Total cost should be based on 32 units (cryomodules) in EDR (8 RF stations operational).  Performance specification is based on 28 units operational (7 RF stations operational).

[2] Qext is a constant for a fixed coupler setting and is independent of Q0.  Here, it is assumed that Qext might be variable.  In theory this would be possible, though difficult in practice.  Alternatively, Qext could be fixed for one set of parameters or a mid value may be set.

[3] R. Boni, G. Cavallari, RF System for the ILC Damping Rings, ILC-LNF-001, Tech. Note, June 2006.

[4] Information provided by M. Palmer (Cornell), 5 October 2006.