ILC Damping Rings Component/Subsystem Specification

Part I – Classification Information

| Component Description: | Electron damping ring RF Cryogenic Plant |
| --- | --- |
| Component Location (beamline): | EDR | Lattice Version: | OCS2, March 2006 |
| Document Number: | EDR-RF-cryp-001 | Date: | 2006-06-12 |
| Prepared by: | Roberto Boni | email: | roberto.boni@lnf.infn.it |
| Technical/Global System: | Cryogenics |  |  |
| Technical/Global System Contact: | Laurent Tavian | email: | laurent.tavian@cern.ch |
| DR Area System Contact: | Susanna Guiducci | email: | susanna.guiducci@lnf.infn.it |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| RF stations operational | 8 | (7) | [1] |
| No. of cryoplants per ring | 4 |  |
| Operating temperature | 4.5 K |  |
| Cryo-losses per beamline | 430 W | (520 W) [2] | [1] |
| Cold-to-warm cryoplant efficiency | 0.03 % |  |
| Wall-plug power per cryoplant | 175 kW |  |
| Unit Cost per cryoplant | Public version: no cost shown | [3] |

Part III – Other Parameters, Information, and Drawings

ILC Damping Rings Component Specification

| Document Number: | EDR-RF-cryp-001 | Date: | 2006-06-12 |
| --- | --- | --- | --- |

Part IV – References

[1]	Total cost should be based on 32 units (cryomodules) in EDR (8 RF stations operational).  Performance specification based on 28 units operational (7 RF stations operational).

[2] This is the cryo-loss of the beam-line if one RF station faults in another beam-line.

[3] R. Boni, G. Cavallari, RF System for the ILC Damping Rings, ILC-LNF-001, Tech. Note, June 2006.