ILC Damping Rings Component Specification Sheet

Part I – Classification Information

| Component Description: | Electron Damping Ring RF System (Overall Summary) |
| --- | --- |
| Component Location (beamline): | EDR | Lattice Version: | OCS2, March 2006 |
| Document Number: | EDR-RF-sys-001 | Date: | 2006-10-09 |
| Prepared by: | Roberto Boni | email: | roberto.boni@lnf.infn.it |
| Technical/Global System: | RF |  |  |
| Technical/Global System Contact: |  | email: |  |
| DR Area System Contact: | Susanna Guiducci | email: | susanna.guiducci@lnf.infn.it |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Working frequency | 650 MHz |  |
| Number of klystron power stations | 8 |  |
| Klystron RF power | 800 kW |  |
| Number of RF cryomodules | 32 |  |
| RF voltage per cavity | 1.45 MV |  |
| RF power per cavity | 109 kW |  |
| Cryogenic temperature | 4.5 K |  |
| Number of cryoplants | 4 |  |
| Wall-plug power per cryoplant | 175 kW |  |
| Waveguide system | WR1500 lines + magic Tee’s + circulators |  |
| Unit Cost | Public version: no costs shown |  |

Part III – Other Parameters, Information, and Drawings

| System | Quantity | Unit Cost (k€) | Total Cost (k€) | Reference |
| --- | --- | --- | --- | --- |
| RF cavity cryomodules | 32 |  |  | Ref: EDR-RF-cav-001 |
| Klystrons | 8 |  |  | Ref: EDR-RF-kly-001 |
| HV Power Supplies | 8 |  |  | Ref: EDR-RF-hvps-001 |
| Cryogenic Plants | 4 |  |  | Ref: EDR-RF-cryp-001 |
| Waveguide Systems | 1 |  |  | Ref: EDR-RF-wvg-001 |
| Low Power Electronics | 1 |  |  | Ref: EDR-RF-lpe-001 |

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-sys-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-sys-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

Important notes:

1.	The alcove dimensions are close to those given in EDR-CONV-alcv-001.

2.	The eight cryomodules in one alcove are sufficient for one ring, assuming four alcoves per ring (i.e. a total of 32 cryomodules).  If two rings are installed in a single tunnel, the size of the alcoves and the ring tunnel will need to be enlarged.

3.	The space available between adjacent components provides for a safe working environment.

ILC Damping Rings Component Specification Sheet

| Document Number: | EDR-RF-sys-001 | Date: | 2006-10-09 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

Part IV – References

[1]	R. Boni, G. Cavallari, RF System for the ILC Damping Rings, ILC-LNF-001, Tech. Note, June 2006.