ILC Damping Rings Component/Subsystem Specification

Part I – Classification Information

| Component Description: | Electron DR Wiggler Vacuum Chamber |
| --- | --- |
| Component Location (beamline): | EDR | Lattice Version: | OCS6, 2006-06-30 |
| Document Number: | EDR-VAC-chmb-003 | Date: | 2006-08-22 |
| Prepared by: | Steve Marks (LBNL) Dave Plate (LBNL) | email: | s_marks@lbl.gov dwplate@lbl.gov |
| Technical/Global System: | Vacuum |  |  |
| Technical/Global System Contact: | John Noonan | email: | noonan@aps.gov |
| DR Area System Contact: | Andy Wolski | email: | a.Wolski@dl.ac.uk |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Quantity per beamline | 80 |  |
| Operating pressure | 1(10-9 torr | [1] |
| Length | 2.75 meter |  |
| Unit Cost | Public version: no costs information shown |  |

Part III – Other Parameters, Information, and Drawings

Keep power density below 15 W/mm2 Keep physical cross sectional size at or below 60mm x 120mm to fit into wiggler cryostat. Length = 2.75 m Absorb wiggler power within wiggler chamber. (Three scenarios have been considered: 1. Absorb power in quad chamber. 2. Absorb power in both chambers. 3. Absorb power in wiggler chambers.) Surface coating for reduction of secondary electrons. (Will be required for the PDR’s, assume coating of all chambers) Currently does not include clearing electrodes. Estimate is based on machined aluminum chamber which includes water cooling to protect wiggler cryostat during NEG regeneration. Bellows transition assembly is included with the quadrupole chamber.

ILC Damping Rings Component Specification

| Document Number: | EDR-VAC-chmb-003 | Date: | 2006-08-22 |
| --- | --- | --- | --- |

Part III – Other Parameters, Information, and Drawings (continued)

| Item | Unit | Units/m | $/Unit | $/m |
| --- | --- | --- | --- | --- |
| Aluminum | Kg | 23.1 |  |  |
| 1Machining (Coarse) | hr | 2 |  |  |
| 1Machining (Fine) | hr | 3 |  |  |
| NEG* | m | 4 |  |  |
| NEG Coating | m | 1 |  |  |
| Stainless Tubing | m | 4 |  |  |
| Tubular Heater | m | 4 |  |  |
| Photon absorber | m | 2 |  |  |
| Welding | hr | 2 |  |  |
| Cleaning | hr | 2 |  |  |
| Fixtures | m | 1 |  |  |
| Total/meter |  |  |  |  |
| Total/chamber 2.75 m |  |  |  |  |

Cross-section of wiggler vacuum chamber.  The chamber is NEG-coated.  NEG-coated “vanes” are shown as yellow cross-hatching.  Water-cooled copper absorbers are shown as red cross-hatching.

ILC Damping Rings Component Specification

| Document Number: | EDR-VAC-chmb-003 | Date: | 2006-08-22 |
| --- | --- | --- | --- |

Part IV – References

[1]	A. Wolski, J. Gao, S. Guiducci, “Configuration Studies and Recommendations for the ILC Damping Rings”, LBNL-59449, February 2006.