ILC Damping Rings Component/Subsystem Specification

Part I – Classification Information

| Component Description: | Arcs and Straights Vacuum System Ion Pumps |
| --- | --- |
| Component Location (beamline): | EDR | Lattice Version: | OCS6, 2006-06-20 |
| Document Number: | EDR-VAC-pmp-002 | Date: | 2006-07-03 |
| Prepared by: | Ron Reid | email: | r.j.reid@dl.ac.uk |
| Technical/Global System: | Vacuum |  |  |
| Technical/Global System Contact: | John Noonan | email: | noonan@aps.anl.gov |
| DR Area System Contact: | Andy Wolski | email: | a.wolski@dl.ac.uk |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Arc cell vacuum pressure (CO) | 0.5 ntorr |  |
| Number of ion pumps per arc cell | 1 |  |
| Arc cell length (ion pump spacing) | 38.9 m |  |
| Arc cell bore | 50 mm |  |
| Arc cell ion pump pumping rate | 20 l/s |  |
| Straight section vacuum pressure (CO) | 0.1 ntorr |  |
| Straight section ion pump spacing | 20 m |  |
| Straight section bore | 50 mm |  |
| Straight section ion pump pumping rate | 20 l/s |  |
| Total number of ion pumps | 208 | [1] |
| Unit Cost per Ion Pump (excluding controllers) | Public version: no cost shown |  |

Part III – Other Parameters, Information, and Drawings

ILC Damping Rings Component Specification

| Document Number: | EDR-VAC-pmp-002 | Date: | 2006-07-03 |
| --- | --- | --- | --- |

Part IV – References

[1]	120 arc cells (1 pump per cell), and 1760 m of straight section (1 pump every 20 m).