ILC Damping Rings Component/Subsystem Specification

Part I – Classification Information

| Component Description: | Electron damping ring injection/extraction septum |
| --- | --- |
| Component Location (beamline): | EDRI | Lattice Version: | OCS6, 2006-06-30 |
| Document Number: | EDRI-INX-spt-001 | Date: | 2006-08-22 |
| Prepared by: | Tom Mattison (UBC) | email: | mattison@physics.ubc.ca |
| Technical/Global System: | Magnets |  |  |
| Technical/Global System Contact: | John Tompkins (FNAL) | email: | jct@fnal.gov |
| DR Area System Contact: | Mike Zisman (LBNL) | email: | mszisman@lbl.gov |

Part II – Main Parameters

| Parameter | Value | Reference |
| --- | --- | --- |
| Field stability | 10-4 |  |
| Thin blade/weak field septum cost | Public version: no costs information shown | [1] |
| Thick blade/strong field septum cost | Public version: no costs information shown | [1] |
| Number of thin blade septa per ring | 2 |  |
| Number of thick blade septa per ring | 2 |  |
| Unit cost per pair (thin and thick blade) of septa | Public version: no costs information shown |  |

Part III – Other Parameters, Information, and Drawings

Costs are based on APS septa, which are pulsed (half-sine-wave pulses, a few hundred microseconds long). Achieving very low ripple during 1 ms ILC pulse will be difficult using pulsed septa. A solution using DC septa could be much cheaper if the injection/extraction optics were modified so that the septum angle could be small. A DC septum might also be shared between injection and extraction with an appropriate optics design.

ILC Damping Rings Component Specification

| Document Number: | EDRI-INX-spt-001 | Date: | 2006-08-22 |
| --- | --- | --- | --- |

Part IV – References

[1]	Cost of APS septa.