# Notes on Lattice Session Discussion

## March 5, 2007

- Central Injector Complex Issues

  - Stacking of Rings

    - Alignment Issues

      - Need evaluation

    - Supports and Stability

      - Need evaluation

    - Survey

      - Review impact of stacked rings

  - CF&S

    - Tunnel Diameter

      - What is minimum acceptable tunnel diameter (presently specified as 4.5m?)

    - Number of shafts

      - Could RTML access tunnel be extended to the presently specified injection/extraction alcoves?

        - Might provide an additional staging point for DR power supplies

        - Apparently a request from PT for a longer access tunnel has already been turned down.

        - This may not be an ideal location for additional DR support hardware

      - It may be time to stop considering further reductions in shafts – it is difficult to imagine only having one for a ring of this size (safety issues?)

      - Need to look at RF configuration

        - How much RF can go in a single straight?

        - Presently do not have enough room for real RF cryomodules in the lattice design.

          - Need longer RF cells:  2.9m per cryomodule!

        - Present plan (16 operating cavities and 9mm bunch length) has 8 cavities on one side and 10 on the other.  The extra pair of cavities is for redundancy/availability issues.

          - For 16 operating cavities, need space for 10 cryomodules in the RF straights

          - For 32 operating cavities (6mm bunch length option), need to allow space for 20 cryomodules in the RF straights

- General Issues

  - Lattice changes to add to baseline

    - Circumference Change

      - Chicane development by ANL

    - Abort dump

      - Location?  Near extraction line?

    - Phase Trombone

    - Lumped Injection/Extraction Kickers

      - Should be implemented in lattice since this appears plausible with current kicker specifications

    - Implement separated injection/extraction straights

    - Add correctors to lattice definition for LET studies

      - Use RDR counts

      - Need to finalize locations

  - Lattice features to study

    - Range of momentum compaction that can be achieved in a given lattice

      - How much flexibility do we have while maintaining reasonable dynamic aperture?

    - Explore harmonic numbers compatible with electron subharmonic buncher

      - Request for someone to take on full review of timing constraint situation and documenting fully

    - Explore optimum layout from technical and cost considerations

      - No. Shafts

      - No. Caverns

      - Options to ease kicker requirements

      - Quantify the impact of changes to the symmetry of the ring

    - Explore how to optimize lattice for beam dynamics considerations and cost  affects momentum compaction factor choice

      - Dynamic Aperture

      - Sensitivity to errors (LET)

      - Collective effects

  - Wiggler region issues

    - Which wiggler parameters should be the baseline?

      - Use results of J. Urban physics optimization?

        - 32 cm period

        - Higher field (1.95T vs 1.67T)

        - Need to verify dependence of energy spread

    - Vertical aperture evaluation

      - Larger aperture provides flexibility for ECE suppression

      - Specify desirable value

    - Radiation fan

      - Generate starting point description of radiation load issues

        - Vacuum chamber wall power densities

        - Straight ahead dump power

        - X-ray scattering into SC wiggler cold mass

      - Is narrower fan due to higher peak field/shorter period good or bad?

      - Need to evaluate vacuum chamber impact for

        - Range of wiggler parameters

        - Design of optics cell

        - Options to mask radiation from VC inside of wiggler?

      - Wiggler Cell

        - Optimize length

        - Add chicanes?

        - Synchrotron radiation dump

    - Wiggler layout

      - Evaluate number of wigglers that can be installed in a row

        - Total power into dump at end of row

        - Vacuum fan power loads on chambers along row

      - Possibly add more short straights between shorter arc sections?

        - Can optimize so that cryogenic transfer lines do not become too long

        - Isolate RF and wiggler straights?

        - Restore ring symmetry