## Slide 1: Recent results of beam tests on clearing electrode and grooves
Y. Suetsugu, KEK

## Slide 2: 1. Clearing electrode
A very thin clearing electrode has been studied at KEK.
A drastic reduction in the electron density around the beam orbit for the electrode voltage of >+300V.
The recent model had basically no heating problem.
In the last autumn run, the almost final version of the electrode was installed into the ring.
  Final beam test of feed through and heating of electrode
2400
Feed through
900
#1 and #2
EBW

## Slide 3: 1. Clearing electrode
A beam pipe with two electrodes was set at a drift space (no magnet)
The temperatures of beam pipe and the surface just behind of electrode were monitored during usual operation.
The electron density was also measured by an electron monitor (drift space).
  Different monitor from the previous strip-type one.
Installed chamber
Inside view
#1
#2
Electrode
Monitor

## Slide 4: 1. Clearing electrode
Electric potential in the test chamber
  ~6 kV/m at the beam orbit, when 500 V is applied to the electrode.
+500 V
+75 V
0 V
  Equipotential lines
Antechamber

## Slide 5: 1. Clearing electrode
Major results:
  Reduction in electron density by a factor of 2 was observed again. Effective for other bunch spacings (4 ~ 16 ns).
  However, the reduction seems less than the case of the previous test chamber. Need further investigation (simulation?).
  Temperature behind the electrode was measured. Estimated input power was ~40 W/m, which is a reasonable value.
  No heating at feed through.
  No degradation in the electrical insulation up to + 1 kV.
  Visually check (2010/1/19); after one month operation
  No crack nor peeling was found. No problem from a functional standpoint.
  But stain-like color change was observed. Stain during cleaning procedure was visually enhanced by electron bombardment?
   Require further monitoring.

## Slide 6: 1. Clearing electrode
R&D Plans ( Beam test: April ~ June)
  Continue the experiment for more 3 months with beams.
  Measurement of electron density at a weak B field (~150 G)
    Using solenoids in hand
    Check the dependence of electron density on B
  More detailed evaluation of impedance

## Slide 7: 2. Grooved surface
Triangular grooves have been also studied at KEK.
  The properties were studied in a wiggler magnet using the same experimental setup to that of the previous clearing electrode.
  B = 0.78 T
Parameters of grooves
  Material: Cu, Al-alloy, SS
  b : 20~30, Rt:0.1~0.2 mm (rectangular)
  d: 2.5~5 mm
Monitor
R47
Y. Suetsugu, H. Fukuma, M. Pivi and L. Wang, NIM-PR-A, 604 (2009) 449
B
  by L. Wang et al.
  Rt
  d
  Al+TiN
  Al
  SS
  Cu
  Inside view
  (Roundness)
  (Depth)
Groove

## Slide 8: 2. Grooved surface
Results: until September, 2009
  b = 20, Rt ~0.1 mm, d = 5 mm, SS, TiN coating (SLAC)
  b = 20, Rt ~0.1 mm, d = 2.5 mm, SS (KEK, discharge machining)
Electron densities for grooves surfaces in these parameters were lower than the case of a flat TiN-coated surface by a factor of ~6.
Availability of grooves was confirmed.
A purpose of experiment in the autumn run was
to investigate applicable structures to large scale production.
(0.9~1.0 mA/bunch)

## Slide 9: 2. Grooved surface
(1) If grooved blocks are welded to a beam pipe (for Cu or Al pipe),
  The machining is available. (low b, small Rt)
  TiN coating is possible separately from beam pipes
  Many welding lines (distortion of chamber, risk of leak), expensive(?)
b = 20, Rt = 0.1 mm
Al + TiN coating
d = 2.5 mm
The reduction in the electron density was larger, by a factor of ~10.
~1x1012 m-3
~1x1013 m-3
~1x1011 m-3
~1x1010 m-3
(0.9~1.0 mA/bunch)

## Slide 10: 2. Grooved surface
(1) Groove blocks are welded to a beam pipe
  Example
Groove block

## Slide 11: 2. Grooved surface
(2) If groove are formed during the extrusion (for Al pipe),
  Relatively large b, large Rt
  TiN coating may be possible, but need R&D
  No welding lines, Cheep (?)
b = 30, Rt = 0.2 mm
Al (A6063)
d = 2.8 mm
Still better than TiN-coated flat surface (even if No coating to Al)
But, the reduction in the electron density was small, by a factor of 3~4.
~1x1012 m-3
~1x1013 m-3
~1x1011 m-3
~1x1010 m-3
(0.9~1.0 mA/bunch)

## Slide 12: 2. Plans for Super KEKB
(2) Groove formed during extrusion
  Example
Groove region
In dipole field

## Slide 13: 3. Grooved surface
R&D Plans (Beam test: April ~ June)
  Manufacturing of two beam pipes with grooved surface is undergoing.
    Welding of groove blocks (machining is possible) [ Cu]
    Extrusion of Al-alloy beam pipe with grooved surface
      We will find the limit of extrusion method in February.
  Beam test of grooved surface with a more realistic structure.
    Assuming the case of Al beam pipe.
  Measurement of SEY for grooved surface in Lab.
    No magnetic field, but we will be able to get some indication.
  More detailed evaluation of impedance
  Any suggestions on our experiments (measurement methods, shape of samples,,,) are welcome for electrodes and grooves!