## Slide 1: MAIN LINAC CRYOMODULE DESIGN REVIEW
INPUT COUPLER

## Slide 2
Bellows
Air Cooling
Waveguide Flange
Cold Ceramic Window
Instrumentation Port
Pump Port
40K Flange
5K Intercept
Cavity
Flange
(2K)
Antenna
(Solid Copper)
Warm Ceramic Window
300K Flange
Most of the Parts:
316 Stainless Steel
with 5m Copper Coating
INPUT COUPLER
40K He Gas
Cooling

## Slide 3
INPUT COUPLER
Operating frequency | 1.3 GHz
Maximum power (CW) | 5 kW
Qext (fixed) | 6.5×107
Cold coaxial line impedance | 70 Ohm
Warm coaxial line impedance | 46 Ohm
Cold coax line outer diameter | 40 mm
Warm coax line outer diameter | 62 mm
Main Parameters of the Coupler

## Slide 4
Heat Load on Cryogenics
 | Static Heat Load | Dynamic Heat Load | Full Heat Load
To 2 K | 0.05 W | 0.06 W | 0.11 W
To 5 K | 0.64 W | 0.32 W | 0.96 W
To 40 K | 3.78 W | 5.94 W | 9.72 W
INPUT COUPLER

## Slide 5
INPUT COUPLER
Parts of Coupler

## Slide 6
INPUT COUPLER
Cryomodule
with Coupler
VAT Valve
Coupler Port
Ion Pump
Cold Cathode Gauge